## Slide 1
APARA C Compiler & Engine Simulator
Handoff: a verified compiler, six simulator fixes, and the evidence behind both
Mohith Kota · APARA C Compiler Project · July 2026

## Slide 2
What is being delivered
• A feature-complete C compiler for the APARA VLIW ISA — used like gcc:
  – git clone → export APARA_TOOLS=… → ./apara-cc prog.c --run
• Verification: 1,300+ programs, every result bit-matched against native gcc
  – 71/71 golden gate · fp01–09 50/50 bit-exact · fuzz: 275 + 613 programs, 0 FAIL
  – Coverage audit: 102/102 (instruction × sub-op × datatype) — nothing untested
• Six simulator source fixes — applied LOCALLY, shipped as a reviewable installer
  – Nothing pushed to the upstream engine repo — approval is today's decision
• A map of remaining engine gaps (reported, not fixed; none affect the compiler)

## Slide 3
Compiler: feature-complete
Every row verified against gcc on the simulator
• Full integer C — all widths, signed/unsigned, all operators
• Structs, unions, bit-fields, enums, statics, goto
• Pointers: arith, &x, p[i], q−p, struct pointers
• Arrays 1D / 2D / 3D, initialized, global + local
• Floating point f32 + f64 — BIT-EXACT vs gcc (50/50)
• Function pointers — via a compile-time linker pass
• Variadic functions and >4 arguments
• Vector intrinsics: $v, $dot, $vreduce, $cmov, $slice, $pack, $fsqrt
• Optimizer:
  – 28-register dynamic allocation + spilling
  – CSE, LICM, loop-carried register promotion
  – VLIW scheduling honoring hardware lane limits
  – up to −74% static bundles on kernels
• Out of scope by design:
  – strings (not needed), NaN compares, u64 ordered compare ≥ 2^63

## Slide 4
How correctness is established
Differential testing: gcc is the oracle, not our own expectations
• Every test writes results[] — the compiler compiles the SAME source with native gcc and records gcc's answers as expected DMEM post-conditions
• The simulator checks every slot: PASS = "produced gcc's values", never "looks right"
• Two fuzz campaigns generate whole programs (UB-free by construction): 1,013 seeds + 13 directed tests
• A coverage auditor scans the emitted mcode of every PASSING program:
  – all 102 instruction × sub-op × datatype combinations proven executed — "leave nothing untouched" is measured, not assumed
• This method found 16 real bugs (10 compiler, 6 simulator) — all fixed, all documented with dates in STATUS.md

## Slide 5
Why the simulator source needed fixes
A compiler cannot be validated against a simulator that computes wrong answers
• Six defects found in engine_isp are OUTSIDE the compiler's control:
  – 3 make ISA instructions silently produce wrong values ($fsqrt→0, unsigned $vreduce, cast masking)
  – 3 are July FP fixes that existed only in binaries and were lost to a rebuild
• "Silently wrong" is the worst case for hardware bring-up: RTL would be validated against a wrong reference
• Every fix is minimal & local — reuses existing machinery, changes no interfaces
• Your tree is untouched: fixes live in my local build + engine_patches/apply_engine_fixes.py (--check / --apply, idempotent, conflict-detecting)

## Slide 6
Fix 1: $fsqrt was an unimplemented stub
MachineRun.cpp : 599 — McodeFsqrtInstruction::Execute
Cause: Execute() was a placeholder; __alu_operation__ already implements __FSQRT via fp_sqrt
Effect: every $fsqrt returned 0 — sqrt(4.0) → 0; hardware would be validated against zeros
Before (search for this text)
McodeRoot::Error("McodeFsqrtInstruction
yet to be implemented", this);
Set_Out_Arg (0, 0);
return;
After (patch applied)
uint64_t ovalue;
___execute_alu_operation___(
Get_Opcode(), Get_Dest_Type(),
Get_Src_Type(), Get_In_Arg(0),
0, 0, 0, ovalue);
Set_Out_Arg (0, ovalue);
After the patch: sqrt(4.0) → 2.0 IEEE-exact (0x4010… → 0x4000…); d08 = 8/8 vs gcc

## Slide 7
Fix 2: float casts → error branch, output UNINITIALIZED
McodeExecute.cpp : 27–33 — ___execute_cast_operation___
Cause: full cast body was guarded by if(neither type is float); float casts fell to an error else
Effect: destination register got host-memory garbage (e.g. 0x7ffd83e474a0) — nondeterministic
Before (search for this text)
if(!dest_type.Get_Float_Flag()
&& !src_type.Get_Float_Flag())
{ /* implementation */ }
else
Error("Float conversions in cast
not supported as yet.");
After (patch applied)
if(1) /* every cast takes the
one real path;
___cast_operation___
dispatches int<->float
itself (Fix 3) */
{ /* implementation */ }
After the patch: fp01–09 = 50/50 bit-exact (with Fixes 3, 4, 6)

## Slide 8
Fix 3: int↔float dispatch called the helpers SWAPPED
McodeOperations.cpp : 330–343 — ___cast_operation___
Cause: plain transposition: int source → cast_float_to_int, float source → cast_int_to_float
Effect: every conversion read its operand as the wrong representation — garbage both directions
Before (search for this text)
if(!src_type.Get_Float_Flag())
w = cast_float_to_int (…);
else if(!dest_type.Get_Float_Flag())
w = cast_int_to_float (…);
After (patch applied)
if(!src_type.Get_Float_Flag())
w = cast_int_to_float (…);
else if(!dest_type.Get_Float_Flag())
w = cast_float_to_int (…);
After the patch: all casts flow through here — verified by the full FP suite

## Slide 9
Fix 4: scalar 32-bit casts masked as if VECTOR casts
McodeOperations.cpp : 314–321 — ___cast_operation___
Cause: is_vector_cast came from in_vals.size()>1 — but Break_Vector splits scalar 32-bit values into 2 entries
Effect: (int)(-6.0f) stored 0x00000000FFFFFFFA — sign extension stripped by the 32-bit lane mask
Before (search for this text)
int is_vector_cast =
(in_vals.size() > 1);
After (patch applied)
int is_vector_cast =
(src_type.Get_Vector_Flag()
&& dest_type.Get_Vector_Flag());
After the patch: fp03 restored 4/4; true vector casts unchanged (both flags set)

## Slide 10
Fix 5: unsigned $vreduce sign-extended its lanes
McodeOperations.cpp : 150–156 — __vreduce_operation__
Cause: shared lane value r was Sign_Extend_64'd BEFORE the signed/unsigned branch; unsigned branch consumed it
Effect: __vreduce_vu8(0x01f2…) = 20 instead of 276 (0xf2 lane summed as −14); wrong unsigned maxima
Before (search for this text)
// sign extend to 64-bits.
int64_t r = (int64_t)
Sign_Extend_64(nbits-1, ele);
if(signed_flag) { … }
else { /* uses sign-extended r */ }
After (patch applied)
uint64_t r = ele; // lane-masked
// = zero-extended
if(signed_flag) {
int64_t r = Sign_Extend_64(…);
… // signed path unchanged
}
After the patch: d06 = 8/8: +/​$max reductions at vi8/vu8/vi16/vu16/vi32/vu32 vs gcc

## Slide 11
Fix 6: cast_int_to_float: C ternary promoted negatives to 2^64−n
McodeFpuUtils.cpp : 437–450 — cast_int_to_float
Cause: cond ? (u & 0xffffffff) : (int)u — the signed arm's int promotes to the unsigned arm's uint64_t
Effect: (float)(-3) became ~1.8×10^19; EVERY negative int→float cast wrong (positives fine — how it hid)
Before (search for this text)
double x =
(src_type.Get_Unsigned_Flag()
? (u & 0xffffffff)
: (int) u);
After (patch applied)
double x;
if(src_type.Get_Unsigned_Flag())
x = (double)(u & __mmask__(snbits));
else {
int64_t sv = ((int64_t)(u <<
(64-snbits))) >> (64-snbits);
x = (double) sv;
}
After the patch: fp03 4/4 (neg & pos int→float, ×, ÷, +); also fixes the hard-coded 32-bit mask

## Slide 12
Process incident — and the safeguards now in place
Why three fixes say “re-applied”
• July 17–18: FP fixes (2, 3, 6) were built & deployed as BINARIES; source stayed pristine
• July 19: rebuilding for the $fsqrt fix regenerated binaries from unfixed source → fixes silently reverted
• The regression gate caught it immediately (fp03 failing, 60/61)
• All six fixes now live IN SOURCE, each with an explanatory comment at the site
• apply_engine_fixes.py --check verifies all six by exact text match; --apply installs on a pristine tree; conflicts (upstream drift) are reported, never guessed
• Standing rule: no fix is ever binary-only; the full gate runs after every rebuild

## Slide 13
Remaining engine gaps — reported, NOT fixed
None affect the compiler: the 102/102 audit proves it only uses the working subset
• NEW FINDING — $vreduce * always returns 0: McodeOperations.cpp:108 (author's TODO) + :161 — accumulator initialized to 0, multiplicative identity should be 1; validity check allows it → silent zero
• f4/f8/f16 float widths: fp_div/fp_sqrt/casts end in assert(0) — McodeFpuUtils.cpp:407/426/460 (loud crash)
• Native $abs/$max/$min broken (compiler lowers to $cmov instead)
• $pack validity checked silently — only a generic "invalid instructions" error (McodeClasses.hpp:412)
• mcode_align emits bundles even after lane-placement ERRORS (CTI not in lane 0 → return into mid-bundle). Recommendation: hard-fail. Compiler bundler now enforces limits itself
• IMEM is ~0x800 words (≈240 bundles) — half the documented size; the one real capacity limit

## Slide 14
Decisions requested today
• 1. Approve the six simulator fixes for the upstream tree
  – apply_engine_fixes.py installs them exactly; or re-type by hand from the report — upstream is untouched until you approve
• 2. Acknowledge the remaining gaps — especially $vreduce * silent-zero and align's emit-on-error
• 3. Hardware validation ownership — repo is self-contained (clone → gate → hardware); any lab member can run it without me
• 4. Confirm whether the half-size IMEM is intentional
Deliverables in hand: APARA_COMPILER repo (compiler + 1,300-program evidence + installer)
Documents: meeting_report.pdf (this deck's full detail, with file:line for every claim) · ENGINE_SOURCE_CHANGES.md