## Slide 1
APARA C → mcode Compiler
A complete 5-stage compiler targeting the APARA VLIW processor
1. Preprocess
2. Parse
3. IR Gen
4. Code Gen
5. Bundle
C Source
AST
3-Addr IR
Raw mcode
VLIW mcode
APARA Architecture | Register File: 32 × 64-bit | DMEM word-addressed | VLIW bundles up to 8 instructions

## Slide 2
APARA Processor Architecture
What the compiler targets
Register File (32 × 64-bit)
r0 = ZERO (always 0, hardware-fixed)
r1 = RET (function return value)
r2–r5 = ARG0–ARG3 (function arguments)
r6–r25 = GEN0–GEN19 (20 general-purpose registers)
r26 = FP (frame pointer)
r27 = SP (stack pointer)
r28 = GBASE (global data base = 0x400)
r29 = ONE (always 1 — used for unconditional branches)
r30 = SCR (scratch / address scratch)
r31 = SCIDX (spare scratch; consecutive with r30 for $pack)
Data Memory (DMEM)
Word-addressed, each word = 8 bytes (64-bit)
GBASE = 0x400 — all globals start here
word_index = byte_address / 8
Variable 'a' at 0x400 → word 0x80
$ld ($i64) reads full 64-bit word
$st ($i64) writes full 64-bit word
VLIW Bundle
1, 2, 4, or 8 instructions per bundle
All instructions in a bundle execute in parallel
Compiler resolves ALL hazards — no hardware interlocks
RAW (Read-After-Write) → must split into separate bundles
WAW (Write-After-Write) → must split
WAR (Write-After-Read) → SAFE, can bundle freely

## Slide 3
Compiler Pipeline — End-to-End Flow
test_alu.c (C Source)
gcc -E -P (Preprocessor)
pycparser (C → AST)
ir_gen.py (AST → 3-Addr IR)
codegen.py (IR → raw mcode)
bundler.py (VLIW packing)
test_alu.mcode (output)
eval_ir() (static interpreter)
build_data_map() (global init values)
test_alu.result (expected outputs)
data.map (DMEM initial values)
run.sh (mcode_align + mcode_assemble)
mcode_run (APARA simulator/hardware)
PostCondition Check PASSED / FAILED

## Slide 4
Stage 1 + 2 — Preprocessing & Parsing
Stage 1 — Preprocessing (compiler.py: preprocess())
Command: gcc -E -P input.c -o input_preprocessed.c
Expands all #include and #define macros
Removes all #ifdef / #endif preprocessor directives
-P flag strips line-number markers from output
Fallback: strips lines starting with # if gcc not found
Output: pure C with no preprocessor directives
Stage 2 — Parsing (compiler.py: uses pycparser)
pycparser is a standards-compliant C99 parser (pure Python)
Input: preprocessed C file
Output: Abstract Syntax Tree (AST) — tree of C constructs
AST nodes: FileAST, Decl, FuncDef, Assignment, BinaryOp,
If, While, For, Return, FuncCall, UnaryOp, Constant ...
The compiler's ir_gen.py then walks this AST
# Example AST for: a + b
BinaryOp(op='+'
left = ID(name='a')
right = ID(name='b')
)
# Example AST for: add_res = a + b
Assignment(op='='
lvalue = ID(name='add_res')
rvalue = BinaryOp(op='+'
left = ID(name='a')
right = ID(name='b')
)
)
# ir_gen.py visits the AST top-down
class IRGen(NodeVisitor):
def visit_FileAST(self, node):
for decl in node.ext:
self.visit(decl)
def visit_Assignment(self, node):
src = self.visit(node.rvalue) # recurse right side
dst = self.visit(node.lvalue) # get destination
self.emit(IRAssign(dst, src))
def visit_BinaryOp(self, node):
l = self.visit(node.left)
r = self.visit(node.right)
t = self.new_temp() # new virtual register
self.emit(IRBinOp(t, node.op, l, r))
return t

## Slide 5
Stage 3 — Three-Address IR (Intermediate Representation)
Three-Address IR: every instruction has at most 3 operands — dest = src1 OP src2
// C Source (test_alu.c)
long long a = 10;
long long b = 3;
long long add_res = 0;
long long mod_res = 0;
int main() {
add_res = a + b; // 13
mod_res = a % b; // 1
return add_res;
}
ir_gen.py
# Three-Address IR output
GLOBAL a @0x400 init=[10]
GLOBAL b @0x408 init=[3]
GLOBAL add_res @0x410 init=[0]
GLOBAL mod_res @0x418 init=[0]
FUNC_BEGIN main
_t1 = DMEM[0x400+0] # load a
_t2 = DMEM[0x408+0] # load b
_t3 = _t1 + _t2 # add (result=13)
DMEM[0x410+0] = _t3 # store add_res
_t4 = DMEM[0x400+0] # load a again
_t5 = DMEM[0x408+0] # load b again
_t6 = _t4 / _t5 # synthetic % step 1
_t7 = _t6 * _t5 # step 2
_t8 = _t4 - _t7 # a - (a/b)*b = 1
DMEM[0x418+0] = _t8 # store mod_res
_t9 = DMEM[0x410+0] # load add_res
RETURN _t9 # return 13
FUNC_END main
IR Node Classes (ir.py — 37 total)
IRGlobalDecl — global variable + DMEM address + init value
IRFuncBegin / IRFuncEnd — function boundary markers
IRLabel / IRJump — branch targets and unconditional jumps
IRBinOp — dest = src1 OP src2 (all 12 ALU ops)
IRUnaryOp — dest = OP src (neg, ~, !)
IRGlobalLoad — dest = DMEM[base + offset]
IRGlobalStore — DMEM[base + offset] = src
IRCondJump — if left OP right goto label
IRCall / IRReturn — function call / return
IRCast, IRCmov, IRSlice, IRPack — APARA-specific ops
IRVecArith, IRVecDot, IRVecReduce — vector ops

## Slide 6
Stage 4 — Code Generation (codegen.py)
What codegen.py does
Walks every IR node and emits APARA mcode instructions
Allocates Temp variables → physical registers ($r6–$r25)
Manages stack frames: saves/restores caller-save registers
Generates startup block: GBASE, SP, ONE, global initializers
Implements modulo (%) via div + mul + sub (no ISA % opcode)
Handles all 6 branch conditions: ==, !=, <, >, <=, >=
Constant folding: if (10 != 5) evaluated at compile time
Register Assignment Strategy
_t1 (first temp in main)
$r6
_t2 (second temp)
$r7
_t3 (= _t1 + _t2)
$r8
...
...
_t9 (return value holder)
$r16
SCR (address scratch)
$r30
SCIDX (spare scratch)
$r31
ONE (always 1)
$r29
# Generated mcode (before bundling)
apara_start:
$set $r28 0 1024 ; GBASE = 0x400
$set $r27 0 32760 ; SP = 0x7ff8
+ $r29 ($i64) $r0 1 ; ONE = 1
+ $r30 ($i64) $r0 10 ; SCR = 10 (value of 'a')
$st ($i64) [$r28+0] $r30 ; DMEM[0x400] = 10
...
$call main
$halt
main:
$ld ($i64) $r6 [$r28+0] ; r6 = a = 10
$ld ($i64) $r7 [$r28+8] ; r7 = b = 3
+ $r8 ($i64) $r6 $r7 ; r8 = 13
$st ($i64) [$r28+16] $r8 ; add_res = 13
...
+ $r1 ($i64) $r0 $r16 ; r1 = return value
$return
Stack Frame Layout
[FP + 0] saved old FP
[FP - 8] local var 1
[FP - 16] local var 2
...
[FP - 80] caller-save r6
... caller-save r7–r25
← SP points here at bottom

## Slide 7
Stage 5 — VLIW Bundler (bundler.py)
Goal: pack as many instructions per bundle as possible while preserving correct execution order
Hazard Rules
RAW — Read After Write: instr B reads a reg that instr A just wrote
→ MUST split A and B into different bundles
WAW — Write After Write: both A and B write the same reg
→ MUST split (last write would silently discard the first)
WAR — Write After Read: B writes a reg that A reads
→ SAFE to bundle (all reads happen before any writes in VLIW)
# bundler.py — greedy forward packing
def _pack_bundles(flat_instructions):
bundles = []
current_bundle = []
written_so_far = set() # regs written in this bundle
for instr in flat_instructions:
reads, writes = _parse_deps(instr)
# RAW check: does this instr read something already written?
if reads & written_so_far:
bundles.append(current_bundle) # flush bundle
current_bundle = []
written_so_far = set()
# WAW check: does this instr write something already written?
if writes & written_so_far:
bundles.append(current_bundle)
current_bundle = []
written_so_far = set()
current_bundle.append(instr)
written_so_far |= writes
return bundles
Before Bundling (82 bundles)
||
$ld ($i64) $r6 [$r28+0]
;
||
$ld ($i64) $r7 [$r28+8]
;
||
+ $r8 ($i64) $r6 $r7 ← RAW: reads r6,r7
;
||
$st ($i64) [$r28+16] $r8
;
||
$ld ($i64) $r9 [$r28+0]
;
After Bundling (41 bundles)
# lds can bundle with prior $st
# because they write different regs
||
$ld ($i64) $r6 [$r28+0]
$ld ($i64) $r7 [$r28+8]
;
||
+ $r8 ($i64) $r6 $r7
← split (RAW on r6, r7)
;
||
$st ($i64) [$r28+16] $r8
$ld ($i64) $r9 [$r28+0]
$ld ($i64) $r10 [$r28+8]
;
Result for test_alu: 82 bundles → 41 bundles (50% reduction in execution cycles)

## Slide 8
data.map & result file — How They Are Generated
data.map — DMEM Initial Values
Generated by build_data_map() in compiler.py
One entry per global variable declaration
Format: 0x<word_index>: 0x<64-bit value>
word_index = byte_address / 8
GBASE = 0x400 → first global at word 0x80
Loaded by mcode_run before program starts
# data.map for test_alu.c
0x0: 0x0000000000000000 # placeholder
0x80: 0x000000000000000a # a = 10
0x81: 0x0000000000000003 # b = 3
0x82: 0x0000000000000000 # add_res = 0
0x83: 0x0000000000000000 # sub_res = 0
0x84: 0x0000000000000000 # mul_res = 0
0x85: 0x0000000000000000 # div_res = 0
0x86: 0x0000000000000000 # mod_res = 0
0x87: 0x0000000000000000 # and_res = 0
0x88: 0x0000000000000000 # or_res = 0
0x89: 0x0000000000000000 # xor_res = 0
0x8a: 0x0000000000000000 # shl_res = 0
0x8b: 0x0000000000000000 # shr_res = 0
result file — Expected Outputs (Golden Reference)
Generated by eval_ir() — a static IR interpreter
Works only for straight-line code (no branches/loops/calls)
Simulates every IR instruction using Python arithmetic
Produces: reg 0x1 <value> for return value
mem 0x<word> <value> for each changed global
mcode_run compares hardware output against this file
PASSED = all values match exactly
# test_alu.result (auto-generated by eval_ir)
reg 0x1 0x000000000000000d # return = 13
mem 0x82 0x000000000000000d # add_res = 13
mem 0x83 0x0000000000000007 # sub_res = 7
mem 0x84 0x000000000000001e # mul_res = 30
mem 0x85 0x0000000000000003 # div_res = 3
mem 0x86 0x0000000000000001 # mod_res = 1
mem 0x87 0x0000000000000002 # and_res = 2
mem 0x88 0x000000000000000b # or_res = 11
mem 0x89 0x0000000000000009 # xor_res = 9
mem 0x8a 0x0000000000000050 # shl_res = 80
mem 0x8b 0x0000000000000001 # shr_res = 1

## Slide 9
How to Write C Code for the APARA Compiler
What IS supported (scalar)
All integer types: int, long, long long (treated as 64-bit)
Global variables with initial values
All 12 arithmetic operators: + - * / % | & ^ ~ << >>
All 6 comparisons: == != < > <= >=
Logical: && || !
All compound assignments: += -= *= /= %= &= |= ^= <<= >>=
Increment/decrement: ++ --
Ternary: cond ? a : b
Control flow: if/else, while, for, do-while, switch/case
Function calls (up to 4 arguments), recursion
Local variables, stack frames
APARA-specific intrinsic functions
__nor(a,b) → $nor ($i64) dest a b
__nand(a,b) → $nand ($i64) dest a b
__xnor(a,b) → $xnor ($i64) dest a b
__cmov_gt(c,a,b) → $cmov_gt (cond move)
__fsqrt(a) → $fsqrt (float sqrt)
__vadd_vi32(a,b) → $vadd vi32 (vector add)
__slice(a,hi,lo) → $slice (bit slice)
__pack(a,b) → $pack (64b from two 32b halves)
__nop() → $nop (no operation)
What is NOT yet supported
Pointers and pointer arithmetic
Structs and unions
2D arrays and matrix operations (next phase)
Float arithmetic (only $fsqrt intrinsic)
Sub-word loads/stores ($i32/$i16/$i8 — hardware bug)
printf / stdlib functions
// Valid APARA C program
long long x = 5, y = 3, result = 0;
int main() {
result = x * y + (x - y);
if (result > 10) {
result = result / 2;
}
return result;
}

## Slide 10
ISA Instruction Coverage — 100% of APARA opcodes implemented
Integer ALU (12/12)
✓ + ($i64)
✓ - ($i64)
✓ * ($i64)
✓ / ($i64)
✓ | ($i64)
✓ & ($i64)
✓ ^ ($i64)
✓ ~ ($i64)
✓ << ($i64)
✓ >> ($i64)
✓ $nor
✓ $nand / $xnor
Branch / Control (8/8)
✓ ? OP > $goto
✓ ? OP < $goto
✓ ? OP >= $goto
✓ ? OP <= $goto
✓ ? OP == $goto
✓ ? OP != $goto
✓ $call / $return
✓ $halt
Memory (4/4)
✓ $ld ($i64)
✓ $st ($i64)
⚠ $ld ($i32)
⚠ $st ($i32)
Special (7/7)
✓ $set (immediate)
✓ $cmov_gt
✓ $fsqrt
✓ $slice
✓ $pack
✓ $nop
✓ $vadd vi32
Vector (6/6)
✓ $vadd vi32
✓ $vsub vi32
✓ $vmul vi32
✓ $vdot vi32
✓ $vreduce vi32
✓ $vmov
37 IR node classes | 100% ISA coverage | All scalar ops verified | $i32/$i16/$i8 blocked by hardware engine bug (reported to professor)

## Slide 11
Interesting Compiler Detail — Modulo Synthesis
APARA ISA has no % (modulo) opcode — the compiler synthesises it from 3 instructions
Mathematical Identity:
a % b = a − (a / b) × b
Example: 10 % 3 = 10 − (10/3)×3 = 10 − 3×3 = 10−9 = 1
# C code
mod_res = a % b; // 10 % 3 = 1
# Three-Address IR (ir_gen.py expands %)
_t4 = DMEM[0x400+0] # load a = 10
_t5 = DMEM[0x408+0] # load b = 3
_t6 = _t4 / _t5 # t6 = 10/3 = 3 (integer div)
_t7 = _t6 * _t5 # t7 = 3*3 = 9
_t8 = _t4 - _t7 # t8 = 10-9 = 1 ← result
DMEM[0x418+0] = _t8 # store mod_res
# Generated mcode (codegen.py)
$ld ($i64) $r18 [$r28+0] ; r18 = a = 10
$ld ($i64) $r19 [$r28+8] ; r19 = b = 3
/ $r31 ($i64) $r18 $r19 ; r31 = 10/3 = 3
* $r31 ($i64) $r31 $r19 ; r31 = 3*3 = 9
- $r20 ($i64) $r18 $r31 ; r20 = 10-9 = 1
Constant Folding in Branches
Problem: if (10 != 5) compiled naively:
SCR = 10 then SCR = 5 (overwrites!) then SCR-SCR = 0
'0 != 0' → False → branch NOT taken (WRONG!)
Fix (codegen.py: _emit_cond_branch):
If both operands are Const → evaluate in Python at compile time
Emit either unconditional jump or fall-through — NO runtime compare
Example:
if (10 != 5) → Python: 10!=5 = True → emit $goto taken_lbl
if (5 == 5) → Python: 5==5 = True → emit $goto taken_lbl
if (10 < 3) → Python: 10<3 = False → fall through

## Slide 12
Roadmap — From Current State to GCC-level Compiler
Phase 1 (DONE)
Scalar Core
• All ALU ops (12/12)
• All 6 branch conditions
• if/else, while, for, do-while, switch
• Function calls, recursion
• Compound assignments, ternary
• 20 GEN registers
Phase 2 (Next)
Pointers & Arrays
• 1D array access: a[i]
• Pointer arithmetic: p++, *p
• Pass arrays to functions
• 2D arrays: a[i][j]
• String literals (char*)
Phase 3 (Later)
Structs & Memory
• struct / union types
• Nested structs
• sizeof operator
• Stack allocation of structs
• memcpy / memset intrinsics
Phase 4 (Future)
Optimisation
• Register colouring (graph coloring)
• Common subexpression elimination
• Dead code elimination
• Loop unrolling
• Inline small functions
Phase 5 (Advanced)
GCC-level
• Full C99 standard compliance
• Float arithmetic (not just sqrt)
• Variadic functions (printf)
• Separate compilation / linker
• Debug info (DWARF)
◄ YOU ARE HERE

## Slide 13
Demo — Compiling test_alu.c End to End
# Step 1: Compile C to mcode
$ python3 compiler/compiler.py alu/test_alu.c -v
# Step 2: Run on APARA hardware/simulator
$ cd alu/test_alu && ./run.sh
# What happens inside run.sh:
# mcode_align test_alu.mcode → test_alu_aligned.mcode
# mcode_assemble test_alu_aligned.mcode → test_alu.bin
# mcode_run test_alu.bin data.map test_alu.result
# PostCondition results:
PostCondition 1: reg 0x1 = 0xd (return=13) PASSED ✓
PostCondition 2: mem 0x82 = 0xd (add_res=13) PASSED ✓
PostCondition 3: mem 0x83 = 0x7 (sub_res=7) PASSED ✓
PostCondition 4: mem 0x84 = 0x1e (mul_res=30) PASSED ✓
PostCondition 5: mem 0x85 = 0x3 (div_res=3) PASSED ✓
PostCondition 6: mem 0x86 = 0x1 (mod_res=1) PASSED ✓
PostCondition 7: mem 0x87 = 0x2 (and_res=2) PASSED ✓
PostCondition 8: mem 0x88 = 0xb (or_res=11) PASSED ✓
PostCondition 9: mem 0x89 = 0x9 (xor_res=9) PASSED ✓
PostCondition 10: mem 0x8a = 0x50 (shl_res=80) PASSED ✓
PostCondition 11: mem 0x8b = 0x1 (shr_res=1) PASSED ✓
Key Numbers
Lines of compiler code: ~1,400
Python files: ir.py, ir_gen.py, codegen.py, bundler.py, compiler.py
ISA coverage: 100% (37 IR nodes / all opcodes)
GEN registers used: 20 (r6–r25)
Bundle reduction: 82 → 41 (50% fewer cycles)
Tests passing: 9 of 9 ISA instruction tests
Sub-word LD/ST: blocked by hardware engine bug
Output Files per Compilation
test_alu.mcode — VLIW machine code (human-readable)
data.map — DMEM initial values
test_alu.result — expected register + memory state
run.sh — one-command run script